Mark

Team name:	A5
Homework number:	HOMEWORK 3
Due date:	16/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	ADC triggered by TIM
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x
Explanation: / We successfully completed the homework. / Part a) ADC triggered by TIM: / CubeIDE Settings: / First we set the output of the potentiometer as an input on our STM32. In specific we set it as the first input to ADC1. PA1 is set to ADC1_IN. / We activate in the “Analog” section the the IN1 in the “Mode” panel and we enable the ADC1 global interrupt in the “NVIC settings” panel. In “ADC_Regular_ConversionMode” tab we set ADC in order to start when there is a TIM10 Trigger Out Event. / We activate the TIM10 and set its channel 1 to “PWM Generation No Output”. This is done in order to start the ADC conversion every time we need (we set the prescaler and the ARR to 8400 and 10000 respectively in order to fill the ARR every 1s). Then under “Trigger Output (TRGO) Parameters” tab we set “Trigger Event Selection” to ‘Update Event’ in order to trigger the Start the ADC conversion when the ARR is filled and the interrupt is generated. / We can check if the UART is activated. It should be active as default and we leave everything as default. / Code: / Some global variables get declared first. Namely the adc_val as uint32, which is the value the ADC produces. Then the float value_volt, which is the voltage value to which the ADC value gets converted. A char buffer of length 20 to store the string we want to send over uart and an uint8 which hold the length of the string. / In the ‘main’ function, the ADC gets started in interrupt mode with ‘HAL_ADC_Start_IT’, so does the timer, with ‘HAL_TIM_PWM_Start’. / All the actual handling happens in the callback function ‘HAL_ADC_ConvCpltCallback’ which is called when the ADC has completed its conversion. / Here the ADC value is read and stored in a variable. Then divided by the maximum ADC value of 4096 and multiplied by the maximum voltage of 3,3. / Next the string to send is created with ‘snprintf’ and sent over Uart through the HAL-function ‘HAL_UART_Transmit’. / And here the magic ends. / Part b) ADC triggered by TIM to LCD: / CubeIDE Settings: / We configure the ADC and the timer like in the previous point / we set the following pins to configure the pinout for the LCD: / PA4: GPIO_Output[LCD_BL_ON] / PB1: GPIO_Output[LCD_E] / PB2: GPIO_Output[LCD_RS] / PB12: GPIO_Output[LCD_D4] / PB13: GPIO_Output[LCD_D5] / PB14: GPIO_Output[LCD_D6] / PB15: GPIO_Output[LCD_D7] / Code: / We import the “PMDB16_LCD” library in the project as follow: / Copy the “PMDB16_LCD.c” file to the /Core/Src folder; / Copy the “PMDB16_LCD.h” file to the /Core/Inc folder; / Add #include "PMDB16_LCD.h“ in main.c; / Then we Initialize the LCD controller using lcd_initialize() and lcd_clear() functions in the main(), before the infinite loop. / In the main() function we initialize the ADC and the timer as before. In the callback function ‘HAL_ADC_ConvCpltCallback’ we first put the ADC conversion value in a string, which is used to show the voltage value in the display (thanks to lcdprint()_ln fuction), then we normalize the ADC result to an integer between 0 and 80. Lastly we use this last variable in the lcd_drawBar() function to plot the bar graph. / Problems encountered: / We have noticed that the ADC value is not stable, indeed if we don’t move the knob, only the first two significative are fixed. We think that this is due to the external noise and the non-ideality of the ADC and the resistor given by the potentiometer. A way to reduce the common mode noise is to add a instrumentation amplifier (INA) having as input the two terminals of the potentiometer.
Professor comments: