Mark	A

Team name:	A5
Homework number:	HOMEWORK 1
Due date:	01/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	Sound detection - LED PWM
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x
Explanation: / Part 1a and b: / To detect the signal from the microphone, we began by consulting the schematic of the "Microcontroller demo board" to identify that the output of the comparator was connected to pin 8 of port A, known as PA8. The subsequent steps involved configuring the necessary interrupt registers through the CubeIDE graphic interface as follows: / We set PA8 as an external interrupt by clicking on it and selecting GPIO_EXTI8. / We activated the external interrupts by choosing EXTI line[9:5] interrupts within the NVIC Interrupt table. / In the GPIO configuration section, we opted for no external pull-up or pull-down resistors, since a pull-up resistor is already present on the "green board" after the comparator's output. Additionally, we selected a rising-edge triggering configuration. / Moving on to setting up PWM for the green LED: / We clicked on pin PA5, which is connected to the LED, and selected TIM2_CH1. / We navigated to the Timers section, selected the TIM2 timer, and configured it for "PWM Generation CH1" on channel 1. / For the subsequent steps, multiple approaches were available. For instance, the external 8MHz clock source can be used as timer clock by selecting the corresponding option in the clock configuration window. Then a prescaler of (127+1) and a counter period of (62499+1) can be chosen in order to achieve a 1-second period. Finally, in the PWM generation menu, a pulse value of 31250 can be selected to achieve a 50% duty cycle. / After generating the code, we proceeded to define the interrupt handler function, "void HAL_GPIO_EXTI_Callback(uint16_t GPIO_Pin)" in the appropriate section of our code. Additionally, we created a variable named "state" in which the PWM state (ON or OFF) will be stored. / The algorithm we wrote works as follow: inside the callback function, we initially check if the pin that triggered the interrupt is PA8, if yes, we toggle the value of the "state" variable, which is used as a boolean. Depending on its value, either the HAL_TIM_PWM_START or HAL_TIM_PWM_STOP functions are invoked. / Both of these PWM functions require two parameters: an handler, automatically generated by the IDE, and the channel identifier "TIM_CHANNEL_1. / Everything works as expected, however the microphone doesn’t always catch the sound. We suspect that: / the threshold set on the circuit is a bit too high / bouncing occurs, producing two (or an even number) subsequent pulses that quickly turn on and off the pwm, not producing a visible effect. / In order to solve the second point, a debouncing effect with an additional timer could be implemented.
Professor comments: