Mark	A

Team name:	A5
Homework number:	HOMEWORK 2
Due date:	06/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	Song
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x
Explanation: / We successfully completed the homework. / Part a: / CubeIDE Settings: / We began by looking in the documentation where was connected the speaker. We started looking in the Green PCB board Schematics, where we found that TIM1_CH2 PWM_SPKR is connected to pin 1 of channel 5 and then in the Nucleo_Schematics that the speaker is connected to the PA9 pin of the microcontroller. / Next step was configure the pin through the CubeIDE as follow: / Click on pin PA9 and select TIM1_CH2 and set the prescaler to 100 in the timer 1 control panel / Set the pin PA8 like GPIO_EXTI_8 and set in the NVIC pannel the EXTI line[9:5] interrupts to enable the interrupt rise from the microphone / Code: / We define a note struct with inside two variables named tmr_period and duration, a play_note function and a play_song function / play_note function needs as input a variable of note type and it sets the period of the PWM (with __HAL_TIM_SET_AUTORELOAD), its duty cycle (with __HAL_TIM_SET_COMPARE) and the duration of the note, which is set using HAL_Delay function / play_song is used to reproduce every note of our song / Part b: / CubeIDE Settings: / We set the pins as before, but in addition in the timer 10 control panel we set the prescaler equal to 8400-1 to set the period division, the ARR equal to 10000-1 to set the counter. With these settings the the timer counter increases every 0,1ms and it is filled in 1s. / Code: / As in the previous point, we define a note struct with inside two variables named tmr_period and duration, a play_note function and a play_song function, but this time we handled the duration of each note with a timer counter / play_note function needs as input a variable of note type and it sets the period of the PWM (with __HAL_TIM_SET_AUTORELOAD), its duty cycle (with __HAL_TIM_SET_COMPARE) and the duration of the note, which is adjusted setting a different value of the timer counter with __HAL_TIM_SET_COUNTER function. Finally this function starts the PWM generation and the timer counter / play_song is used to reproduce every note of our song / HAL_TIM_PeriodElapsedCallback is used to turn off the PWM generation when the note has ended its time and a flag is raised in order to procede with the next note
Professor comments: