Mark

Team name:	A5
Homework number:	HOMEWORK 3
Due date:	16/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	UART w/ DMA & LCD
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x
Explanation: / We successfully completed the homework. / Part a UART w/ DMA: / CubeIDE Settings: / First we set up the USART protocol in the connectivity → USART2 menu, by setting it up as asynchronous, with a baud rate of 115200 bit/s, 8 bit word length, no parity, and one stop bit. / To setup the DMA peripheral, in the system core → DMA menu, we first added a new element, and then set it up as USART2_TX with direction “memory to peripheral” and data width one byte. / We also activated the timer10 and its global interrupt, by setting a 1s period, like in the previous homework, just to have a more readable serial data monitor. / In the NVIC interrupt table we activated the “DMA1 stream6 global interrupt” and the “USART2 global interrupt”, the latter is needed otherwise the DMA peripheral will stop after sending the first packet. / Code: / First a “uint8_t buff[]” string is initialized with the name and date that we want to send over UART protocol. / In the “int main(void)” function, before the infinite loop, we start the timer in interrupt mode thorugh the “HAL_TIM_Base_Start_IT()” function. No code is present inside the infinite loop, in fact all the operations are handled in the interrupt service routine triggered by the timer every 1 second. In the “HAL_TIM_PeriodElapsedCallback()” interrupt routine, first we check that it is the timer10 that has effectively triggered the interrupt, and if yes, first we stop the timer, and then we get the status of the UART bus with the function “HAL_UART_GetState()”. If the UART is ready to send new data, we send it through the DMA peripheral by calling the function “HAL_UART_Transmit_DMA()”, which requires as arguments: the UART2 handler, the buffer buff[], and the length of the buffer, which we recover through the “strlen()” function. Lastly, we restart the timer in interrupt mode. / Part b LCD: / CubeIDE Settings: / Set the internal clock (in this case TIM10) at frequency 1 Hz (Prescaler = 8400-1, Counter Period = 10000-1) to trigger a PeriodElapsed Interrupt every 1 second. / In the NVIC interrupt table, activate the TIM10 global interrupt / Set the following pins to configure the pinout for the LCD: / PA4: GPIO_Output[LCD_BL_ON] / PB1: GPIO_Output[LCD_E] / PB2: GPIO_Output[LCD_RS] / PB12: GPIO_Output[LCD_D4] / PB13: GPIO_Output[LCD_D5] / PB14: GPIO_Output[LCD_D6] / PB15: GPIO_Output[LCD_D7] / Code: / We import the “PMDB16_LCD” library in the project as follow: / Copy the “PMDB16_LCD.c” file to the /Core/Src folder; / Copy the “PMDB16_LCD.h” file to the /Core/Inc folder; / Add #include "PMDB16_LCD.h“ in main.c; / Then we Initialize the LCD controller using lcd_initialize() and lcd_clear() in the main() function, before the infinite loop. / For the main() function we initially display the first group member* in the row 1 (second row of lcd) using the function lcd_println (char string[], uint8_t row), then using the same print function each timer interrupts we iterativelly: / print the current squad member at the row 0 (first row); / print the next squad member **, at the row 1 (second row). / * Each member’s name is contained in alphabetical order in the Array “group”. / ** Or the first one if we arrived at the last one to restart the cycle.
Professor comments: