Mark	A

Team name:	A5
Homework number:	HOMEWORK 2
Due date:	06/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	IR Comunication
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x
Explanation: / We successfully completed the homework. / Idea: / The idea is use the IR led and the IR reciver placed on the bord in order to comunicate each other using a UART protocol and comunicate which button on the tx board was pressed showing the correspondent symbol on the led matrix of the rx board. / IR Transmit: / Looking at the schematics of the green board we can see that the PB10 is connected to a bjt that controll the IR_LED. Following the schematics we can understand that when the PB10 is high the bjt short the IR_LED and it is off, instead when the PB10 is low the IR_LED is on. / CubeIDE Settings: / we set the PB10 like an output / we set PC2, PC3, PC12 and PC13 like GPIO_EXTIx (with falling edge detection) and PC8,PC9,PC10,PC11 as GPIO_Output in order to control the keyboard. / Enable the timer10 that we used in order to enable the column of the keyboard and the timer11 used for the data trasmission and enable the corresponding interrupt in the NVIC table. / Code: / On the base of the code of the HOMEWORK_09 we scan the 4x4 keyboard looking for a pressed button. When a button is press we enable the transmission starting the timer11. Every time a interrupt generated by the timer11 is detected, we send a bit. In order to start the UART comunication with the receiver board we have to send a low value, then we can send the seven bit data, the parity bit and the stop bit. / IR Receive: / The receiver board has to save the data sent by the other board in a variable that is used to display the character (corresponding to the key pressed on the transmitter keyboard) on the led matrix. / CubeIDE Settings: / we set the pin PB6 as GPIO_Output / we set the pin PA10 as GPIO_EXTIx / we set PA5 as SPI1_SCK, PA7 as SPI1_MOSI and we configured the SPI like in homework 7, with its DMA / we configured timer2 in order to raise an interrupt flag every 2.5 s, timer3 every 2.3 ms and timer10 every 42 ms / eventually we enabled the required interrupts in the NVIC interrupt table / Code: / Thanks to HAL_GPIO_EXTI_Callback() function we raise a flag that let us start the communication in the while, indeed as soon as the first bit is received, the timer 10 is started and when its ARR is filled, the bit_counter variable is increased. This variable helps us to keep track of the number of bits received and every time it is increased, a new value is added in the payload variable, which contains the data we are receiving. The interval of time between the arrival of two bits is set to 42ms, a bit lower than the suggested maximum 0.417 ms (2400bps) and this timing must be equal for both transmitting and receiving boards. / At the end of each iteration both UART_started_flag and tim_elapsed variables are set to 0, in order to enter in the if only when a new data has been received. When also the stop bit arrived, payload is reset, as well as the flags and the timer10 is stopped. / We put a few HAL_UART_Transmit() functions in order to debug the code. / The variable payload is filled with the bit_val value read thanks to HAL_GPIO_ReadPin() function and shifted in the position needed. / Eventually we add the code of the lab 7 slightly modified, in order to display the desired character on the led matrix and clear the matrix if no data is received for more than 2.5 seconds.
Professor comments: