Mark

Team name:	A5
Homework number:	HOMEWORK 7
Due date:	19/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	LED Matrix with SPI
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x

Explanation: / We successfully completed the homework. / Part a) Transmit a letter to the LED matrix using SPI and a timer interrupt: / The idea is to send through SPI the information needed to update the LEDs matrix, i.e. we send the data corresponding to a new column every 4 ms and then we toggle the RCLK signal from LOW to HIGH in order to update the shift register’s outputs. / CubeIDE Settings: / First we enable the pin PA5 for the SPI clock, the pin PA7 for the SPI MOSI and the pin PB6 for the RCLK, which toggles the storage registers. The MISO pin is not needed (since we only need to send data to the slave), as well as the slave select, since shift registers are always enabled. / In the SPI1 Mode and Configuration we set the mode Transmit Only Master and we set the Prescaler to 4. / We set a timer which fills its ARR in 4 ms and we activate the global interrupt of the timer. / Code: / We declared a uint8_t vector containing the coordinates of the matrix as follows: the first two elements tell the shift registers which LEDs must turn on and for which column (the first in this case), the third and the fourth elements tell the shift registers which LEDs must turn on and for which column (the second in this case) and so on.[1] Then we declared a variable that stores the index of the vector. / In the core of the code, we initiate a timer in interrupt mode using the HAL_TIM_Base_Start_IT() function. Within the ISR HAL_TIM_Period_ElapsedCallback(), which is invoked each time the timer's ARR is filled, the following operations are performed: we first check which timer triggered the interrupt. Subsequently, the RCLK pin is set to a LOW state. The row and column information is then transmitted via SPI with the HAL_SPI_Transmit() function, ensuring that all new data is loaded into the shift registers. Next, the RCLK pin is set to a HIGH state, allowing the passage of data to the output of the shift registers. Finally, the index variable is incremented by 2 (since we transmit two bytes through SPI), and if the last index is reached, it is reset to 0. / Part b) / CubeIDE Settings: / The SPI pins are set like in the previous point. The DMA2 Stream3 is emploied to manage the SPI comunication. Besides TMR10, now also TMR2 is emploied to switch between letters. Its ARR is filled every seconds. / Code: / We have initialized the same set of variables as in the previous point, and subsequently introduced additional components to enhance functionality. Specifically, we've introduced: / a char vector named "Word" that contains the ASCII characters of the symbols we want to display on the LED matrix. / An integer variable, "index_word," has been included to keep track of the character currently being displayed. / A vector containing the row and column information about a second character has been incorporated, along with a uint8_t pointer “buffer”. This pointer efficiently references one of the symbols vectors, eliminating the need for redundant vector copies and saving both time and memory. / The interrupt service routine (ISR) for timer 10 remains similar to the previous version, with notable changes in the SPI function. This time, we have employed the HAL_SPI_Transmit_DMA() function, which operates in a non-blocking manner. Consequently, it is imperative to wait for the completion of communication before setting RCLK high. The waiting process, with interrupt, is managed through the HAL_SPI_TxCpltCallback() function, ensuring that RCLK is pulled HIGH only after communication completion. / Regarding the ISR for Timer 2, a switch-case structure has been employed. The integer variable "index_word" serves as an indicator of which ASCII symbol from the "Word" array is intended for display on the LED matrix. Based on the value of "index_word," the "buffer" pointer is dynamically adjusted. It is assigned the value of the pointer pointing to the first element of either of the two arrays containing rows and columns data. With each interrupt triggered, the value of "index_word" is incremented. Consequently, at each interrupt occurrence, a new symbol from the "Word" array is selected for display on the LED matrix. This incremental change in "index_word" ensures a periodic update, with a new symbol appearing every second as a result of the interrupt-triggered increments.
Professor comments:
[1] Althoug if in this first point it is not visible, the even elements are always the same, so the column turn-on order does not change.