Mark

Team name:	A5
Homework number:	HOMEWORK 4
Due date:	22/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	ADC triggered by TIM
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x
Explanation: / We successfully completed the homework. / Part a) ADC triggered by TIM: / CubeIDE Settings: / First we set the output of the potentiometer as an input on our STM32. In specific we set it as the first input to ADC1. PA1 is set to ADC1_IN. / In the “Analog” section we activate the IN1 from the “Mode” panel and then we enable the ADC1 global interrupt in the “NVIC settings” panel. In the “ADC_Regular_ConversionMode” tab we enable “Timer 2 trigger Out Event” such as the conversion will start when an interrupt from the TIM2 is raised. / We activate the TIM2 and set its channel 1 to “PWM Generation No Output”. This is done in order to start the ADC conversion every time we need (we set the prescaler and the ARR to 8400-1 and 10000-1 respectively in order to fill the ARR every 1s). Then under “Trigger Output (TRGO) Parameters” tab we set “Trigger Event Selection” to “Update Event” in order to trigger the Start of the ADC only when the counter register reaches 10000 (1s). / We check if the UART is activated. It should be active as default and we leave everything as default. / Code: / Some global variables get declared first: namely the “adc_val” as uint32, which is the value the ADC produces. Then the float “value_volt”, which is the voltage value to which the ADC value gets converted. An array of chars “buffer” of length 20 to store the string we want to send over uart and an uint8 “length” which holds the length of the string. / In the “main” function, the ADC gets started in interrupt mode with “HAL_ADC_Start_IT”, so does the timer, with “HAL_TIM_PWM_Start”. / All the actual handling happens in the callback function “HAL_ADC_ConvCpltCallback” which is called when the ADC has completed its conversion. Here the ADC value is read and stored in a variable, then divided by the maximum ADC value of 4096,0 and multiplied by the maximum voltage of 3,3. It’s important to keep the ,0 after the 4096 such as to tell the compiler that it’s a float operation. Next the string to send is written in the buffer with “snprintf” and sent over uart through the HAL-function “HAL_UART_Transmit”. / And here the magic ends. / Part b) ADC triggered by TIM to LCD: / CubeIDE Settings: / We configure the ADC and the timer like in the previous point / we set the following pins to configure the pinout for the LCD: / PA4: GPIO_Output[LCD_BL_ON] / PB1: GPIO_Output[LCD_E] / PB2: GPIO_Output[LCD_RS] / PB12: GPIO_Output[LCD_D4] / PB13: GPIO_Output[LCD_D5] / PB14: GPIO_Output[LCD_D6] / PB15: GPIO_Output[LCD_D7] / Code: / We import the “PMDB16_LCD” library in the project as follow: / Copy the “PMDB16_LCD.c” file to the /Core/Src folder; / Copy the “PMDB16_LCD.h” file to the /Core/Inc folder; / Add #include "PMDB16_LCD.h“ in main.c; / Then, we initialize the LCD controller using the "lcd_initialize()" and "lcd_clear()" functions in the "main()" function, before entering the infinite loop. In the "main()" function, we also start the ADC and the timer exactly as before. / In the callback function "HAL_ADC_ConvCpltCallback," we first store the ADC conversion value in a uint32 variable, which we then use to calculate the floating-point voltage, following the same operations as before. We convert this value into a string and write it into a buffer using the "snprintf()" function. The string is then used to display the voltage value on the LCD with the "lcdprint_ln()" function. Additionally, we convert the ADC value into an integer ranging from 0 to 80 to correctly plot the bar graph using the "lcd_drawBar()" function. / Problems encountered: / We have noticed that the ADC value is not stable, indeed if we don’t move the knob, only the first two significative digits are fixed. We think that this is due to the external noise, internal electronic noise and the non-idealities of the ADC. A way to reduce the common mode noise would be to add a instrumentation amplifier (INA) having as input the two terminals of the potentiometer, followed by a LPF to reduce the noise bandwidth.
Professor comments: