Mark

Team name:	A5
Homework number:	HOMEWORK 8
Due date:	26/11/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	Encoder 1a & 1b
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x

Explanation: / We successfully completed the homework. / Part a) Encoder readout / CubeIDE Settings: / First we set the pins PC6 and PC7 respectively as CH1 and CH2 of the TMR3. / In the timer section, we activate TMR3 in “Encoder Mode” through the “Combined channels” menu. / The parameters must be set as follow: internal clock division by 4, polarity of first channel as rising edge, polarity of second chanel as falling edge and filter set to 15 for both channels. Setting the filter to 15 activates a 12.2us digital filter, mitigating spurious pulses resulting from contact bouncing. We set CKD to 4 in order to further decrease the frequency of the sampling (fDTS=fclk/CKD and for our filter configuration fsampling=fDTS /32). / The pulses emitted from the two outputs of the encoder are quadrature-encoded, meaning that when the incremental encoder is moving at a constant velocity, the output waveforms are square waves and there is a 90 degree phase difference between them. In order to specify to the STM32 how to define the sign of the phase difference between our 2 channels, we use the polarity settings. / The timer will extract a clock from the two channels active edges and will increment or decrements its register accordingly. The polarity of the two channels is configured in order to have a counter increment if the encoder is rotated clockwise and a decrement if rotated counterclockwise; indeed the channel 1 generates a square wave +90° phase-shifted (with respect to channel 2) in the first case and -90° phase-shifted otherwise. / USART2 is activated in asynchronous mode, with the following configurations: / Code: / Before the infinite loop, we start the timer in encoder mode with the HAL_TIM_Encorder_Start() function, then in the while(1) loop, we first save the content of the counter register into a int16 variable called “curr_count” using the __HAL_TIM_GET_COUNTER() function. / To determine the number of "ticks" the encoder has experienced in the past second, we first read the actual value of the TIM register, we calculate the delta by subtracting the past value from the actual one, and then we store the current value in the “previous value” variable before idling the system for 1 second. / To address potential overflow and underflow issues, we use int16_t for the "current" and "previous" variables, as well as the "delta" variable. This choice ensures that the subtraction operation between two 16-bit variables, considering 2's complement, effectively discards the 17th bit, preserving only the necessary LSBs and eliminating detrimental information from larger bits (17th and beyond). This ensures correct delta computation even across overflow/underflow conditions. / The reason why it works is simple: when the counter overflows, it goes back to 0b0000_0000_0000_0000 (instead of 0b1_0000_0000_0000_0000 if it was a variable 17 bits long) and performing a subtraction between this value and a number smaller or equal to 0xFFFF (which is the last value before the counter overflows), we obtain the correct result. / For example if the counter overflows to 0x0000 and the previous value is 0xFFFF, the difference is computed as follows: the subtrahend is transformed in its 2’s complement (0x0000), the result is added to 1 (obtaining 0x0001) and finally added to the initial minuend, so the final result is 0x0001 and it is correct, even though an overflow happened.[1] / Similarly if an underflow happens, the counter value from 0x0000 becomes 0xFFFF and thanks to the properties of the operations among signed 2’s complement variables, the delta computed is correct. The key point in this case is that the variables we use are signed, so as soon as the counter underflows we get a value that converted in int16_t is equal to “-1” (while the timer considers these values unsigned, i.e. “65535”) and it is easy to see that after underflow every decrement of the counter lead to a decrement in both the views: the timer sees “0” → ”65535” → ”65534”, while in a signed representation we see “0” → “-1” → “-2”. / We then multiply the delta by 60 (the seconds in a minute) and divide it by 24 (the maximum number of ticks per revolution) to compute the speed in rounds per minute. Finally, we send the calculated value to the PC via UART. / Part b) Encoder readout with TMR and DMA / CubeIDE Settings: / TMR3 settings are the same as before (encoder mode) / TIM10 is enabled and configured such as an interrupt is generated every second (PSC = 4800-1, Period = 10000-1). / the SPI pins are set like in the previous point. The DMA2 Stream3 is employed to manage the SPI comunication. Besides TMR10, now also TMR2 is employed to switch between letters. Its ARR is filled every second. / USART2 is activated in asynchronous mode, as in the previous point. / We employ one DMA controller for the USART2. We configure it to operate in "normal" mode with direction as “memory to peripheral". / Under “System Core” tab we set in the NVIC section both the USART2 global interrrupt and the TIM10 global interrupt. The DMA interrupt is automatically set. / Code: / The mechanism is the same as the point before, with the only difference that the code that calculates the RPM speed is executed in the TIM10 ISR, and that the HAL_UART_Transmit_DMA() function is employed.
Professor comments:
[1] If the minuend was bigger than 0x0000 (for example 0x00XX), the result of the difference would be greater (for example 0x00XX bigger). This is absolutely not a demonstration, but it should work fine in any case.