Mark	A

Team name:	A5
Homework number:	HOMEWORK 2
Due date:	06/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	IR Comunication
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x
Explanation: / We successfully completed the homework. / Idea: / The idea is use the IR led and the IR reciver placed on the bord in order to comunicate each other using a UART protocol and comunicate which button on the tx board was pressed showing the correspondent symbol on the led matrix of the rx board. / IR Transmit: / Looking at the schematics of the green board we can see that the PB10 is connected to a bjt that controll the IR_LED. Following the schematics we can understand that when the PB10 is high the bjt short the IR_LED and it is off, instead when the PB10 is low the IR_LED is on. / CubeIDE Settings: / we set the PB10 like an output / We set PC2, PC3, PC12 and PC13 like GPIO_EXTIx (with falling edge detection) and PC8,PC9,PC10,PC11 as GPIO_Output in order to controll the keyboard. / Enable the timer10 that we used in order to enable the column of the keyboard and the timer11 used for the data trasmission and enable the corresponding interrupt in the NVIC table. / Code: / On the base of the code of the HOMEWORK_09 we scan the 4x4 keyboard looking for a pressed button. When a button is press we enable the transmission starting the timer11.Every time a interrupt generated by the timer11 is detected, we send a bit. In order to start the UART comunication with the reciver board we have to send a high value, after we can send the seven data bit and after the parity bit and the end comunication bit. / IR Recive: / CubeIDE Settings: / Code:
Professor comments: