Mark

Team name:	A5
Homework number:	HOMEWORK 9
Due date:	16/10/2023

Contribution	NO	Partial	Full
Luca Daidone			x
Leonardo Ritter			x
Luca Cordaro			x
Lorenzo Strechelli			x
Ignazio Neto Dell'Acqua			x
Notes:

Project name	4x4 keyboard
Not done	Partially done (major problems)	Partially done (minor problems)	Completed
			x

Explanation: / We successfully completed the homework. / Part a) Scan each column and read the keyboard using polling: / The idea is to pull down a column at a time, every 10 ms (the other columns are set to a high level) and check if an input pin has been driven low, i.e. if a button is pressed. / CubeIDE Settings: / First we set PC2,PC3,PC12,PC13 as GPIO_EXTI (with falling edge trigger detection) and PC8,PC9,PC10,PC11 as GPIO_Output. Eventually we set the EXTI lines interrupt required and the USART global interrupt. / Code: / We added the library “time.h” in order to use the HAL_GetTick() function. We declared a global int variable, i, in order to have a column index, a global uint32_t 4x4 matrix, press_time, containing the time that passed since one button is pressed and a string for the character is going to be sent through UART. / In the main we filled the matrix with the maximum value, i.e. 2^32, in order to avoid to print two times the character at the beginning. In the while loop we turn on one column at a time using a HAL_Delay() function. / In the EXTI callback function we select which row has been pulled down with a switch case structure, we measure the actual time with the HAL_GetTick() function and we print the character corresponding to the key pressed only if more than 60 ms passed between one callback and the other. With 60 ms we avoid to send multiple times the same character if we keep the buttton pressed for more than 40 ms, indeed the time difference is about 40 ms and it is well below 60 ms. / Part b) / CubeIDE Settings: / We set pins PC8,PC9,PC10,PC11 as before, but then we also configured a timer that fills up its ARR in 10 ms, to avoid using HAL_Delay() function. In the NVIC Interrupt table we added the timer global interrupt. / Code: / The code is the same as before, except for the fact that we while loop is empty and the columns are turned off in the timer ISR. / Problems encountered: / In the second point we had to add a -1 before printing the keyboard value in order to obtain the correct character. We think this bug is due to the fact that the timer ISR blocks the EXTI callback function and adds a +1 to the variable i before the UART function is finished.
Professor comments: